Sound Devices 552 Field Mixer

Quick Start

DEFAULT:

- 2 Tracks

- 48kHz Sample Rate

- 24 Bit depth

- Broadcast Wave File

- No Timecode; requires external timecode source (TC input, TC IN solid blue)

- Can record WAV or MP3 files

- Has 5 inputs with 2-stage Gain: input trim and fader (larger knob), continuously variable pan (top right knob) and continuously variable high-pass (bottom right knob).

- Direct Outputs, pre or post fade selectable, set up in the set-up menu.

- 5 input limiters and 2 mix output limiters

- Outputs: XLRs, Hirose 10-pin, and TA3 connections

- XLRs can be AES output A and B to interconnect directly to cameras that accept AES3.

- AES3 (also known as AES/EBU) is a standard for the exchange of digital audio signals between professional audio devices. AES3 was jointly developed by the Audio Engineering Society (AES) and the European Broadcasting Union (EBU). An AES3 signal can carry two channels of PCM audio over several transmission media including balanced lines, unbalanced lines, and optical fiber.[1] It was published in 1985 and has been revised in 1992 and 2003. AES3 has been incorporated into the International Electrotechnical Commission's standard IEC 60958, and is available in a consumer-grade variant known as S/PDIF.

- Can connect timecode to the unit.

QUICK START

- Make sure to have a formatted SD Card inserted.

- Turn on at top right switch.

- LEDs should light up green and stop at one lit green one.

- For Line Level (Mic), toggle Mic/Tone to Mic Line.

- For Phantom Power, push the PFL to the left and toggle to Tone. Blue PH light should light up.

- GAIN: Set Master Volume at Unity. Set Fader Black Knob to Unity and turn up the input Trim knob to adjust GAIN until meters show a proper signal (12dB max, no red/distortion in meter).

- To minimize unwanted Low Freq Noise, use the adjustable high-pass filter (small black knob at bottom).

- Choose AES A Source Menu

- Choose Timecode

- Press up on the REC button to record

- Press the REC button to stop recording.

- Scroll left/right, move REC button down to play to listen to files.